#### COAL - SAP 1 Architecture
Ali Muzahir
(P18-0058)
To understand the internal behavior of CPU, Albert Paul Malvino designed a simple model for understanding the basic functionality of Microprocessor. That design he presented is called “Simple as Possible Processor” or in short SAP. The SAP-1 design contains the basic necessities for a functional Microprocessor. Its primary purpose is to develop a basic understanding of how a microprocessor works, interacts with memory and other parts of the system like input and output. The instruction set is very limited and is simple.
INSTRUCTION SET:

The instruction format of SAP-1 Computer is:
(XXXX) (XXXX)
The first four bits make the op-code while the last four bits make the operand (address).

Features:
The architecture is 8 bits and comprises of 16 X 8 memory i.e. 16 memory location with 8 bits in each location, therefore, need 4 address lines which either comes from the PC (Program Counter which may be called instruction pointer) during computer run phase or may come from the 4 address switches during the program phase. All instructions (5 only) get stored in this memory. It means SAP cannot store program having more than 16 instructions.

SAP can only perform addition and subtraction and no logical operation. These arithmetic operations are performed by an adder/subtractor unit. There is one general purpose register (B register) used to hold one operand of the arithmetic operation while another is kept by the accumulator register of the SAP-1. In addition, there are 8 LEDs which work as output unit and connected with the 8 bit output register. All timely moment of data or activities are performed by the controller/sequencer part of the SAP-1.

Program Counter
- It counts from 0000 to 1111.
- It signals the memory address of next instruction to be fetched and executed.
Inputs and MAR (Memory Address Register)
During a computer run, the address in PC is latched into Memory Address Register (MAR)
RAM
- The program code to be executed and data for SAP-1 computer is stored here.
- During a computer run, the RAM receives 4-bit addresses from MAR and a read operation is performed. Hence, the instruction or data word stored in RAM is placed on the W bus for use by some other part of the computer.
- It is asynchronous RAM, which means that the output data is available as soon as valid address and control signal are applied.
Instruction Register
IR contains the instruction (composed of OPCODE+ADDRESS) to be executed by SAP1 computer.
Controller-Sequencer
- It generates the control signals for each block so that actions occur in desired sequence. CLK signal is used to synchronize the overall operation of the SAP1 computer.
- A 12-bit word comes out of the Controller-Sequencer block. This control word determines how the registers will react to the next positive CLK edge.
Accumulator
- It is a 8-bit buffer register that stores intermediate results during a computer run.
- It is always one of the operands of ADD, SUB and OUT instructions.

Adder/Subtractor
- It is a 2's complement adder-subtractor.
- This module is asynchronous (unclocked), which means that its contents can change as soon as the input words change.
B-register
It is 8-bit buffer register which is primarily used to hold the other operand (one operand is always accumulator) of mathematical operations.
Output Register
This registers hold the output of OUT instruction.
Binary Display
- It is a row of eight LEDs to show the contents of output register.
- Binary display unit is the output device for the SAP-1 microprocessor.
Fetch and Execution Cycle of SAP-1 instructions
- SAP-1 instruction cycle: 3 clock cycles to fetch and decode phase, 3 clock cycles to execute
- The first three states are:
  1. address
  2. increment
  3. memory
- Controller has a 6-bit ring counter which continuously cycles from 000001 up to 100000 then resets (must be set to 000001 when we initialize the computer)
- Ring counter is clocked on clock high-to-low transition, most of the other circuits in the computer on clock low-to-high transition
Fetch Cycle
- Address state: enable PC to bus three-state output, MAR load line
- Increment state: enable PC increment
- Memory state: enable memory CE, IR load line
- IR is loaded on the low-to-high clock transition
  t1: MAR ← PC
  t2: PC ← PC +1
  t3: IR ← RAM

Execution Cycle -- LDA
- state 4: enable IR to bus three-state output, MAR load line
- state 5: enable memory CE, accumulator load line
- state 6: enable nothing
  t4: MAR ← (IR (Address of operand))
  t5: Accumulator ← RAM
  t6: nothing
Execution Cycle -- ADD
- state 4: enable IR to bus three-state output, MAR load line
- state 5: enable memory CE, register B load line
- state 6: enable add, ALU to bus three-state output, accumulator load line
  t4: MAR ← (IR (Address of B))
  t5: B ← RAM
  t6: Accumulator ← Accumulator + B
## Assembling of code in memory:
Let take an example of arithmetic problem in assembly language translate into a equivalent machine code using the Opcode given in the above instruction table.
Example: 21H – 02H + 0AH
Memory Addresses	Assembly code	Machine code (binary)
0H	LDA 8H	0000 1000
1H	SUB 9H	0010 1001
2H	ADD AH	0001 1011
3H	OUT	1110 xxxx
4H	HLT	1111 xxxx
5H
6H
7H
8H	21H	0010 0001
9H	02H	0000 0010
AH	0AH	0000 1010
BH
CH
DH
EH
FH